## Slide 1: How AI Accelerates Research and Engineering in Nuclear Fusion Dr. Gilles Fourestey Operational director SCientific IT and Application Support Platform (SCITAS) EUROfusion Advanced Computing Hub EPFL AI + Astronomy Workshop 03/2026
Credit: Nasa/Peter L. Dove.

## Slide 2: Fusion research is moving fast
.2 mg of fuel = 2 litres of petrol
69 MJ/20 kWh
https://www.youtube.com/watch?v=hQVzroA9qsE
In 2024, JET (UK) produced deuterium-tritium fusion for 5 seconds

## Slide 3: What is fusion?
Fusion is the energy of the stars…
It is a form of nuclear reaction
In fusion, light atoms are fused together
It releases a huge amount of energy (E = mc2)
It releases no CO2 and intrinsically safe
Problem:
The deuterium and tritium nuclei are positively charged, Coulomb repulsion applies
Even in the sun, it is incredibly rare. At:
10 Million degrees Kelvin
100 billion atmospheric pressure
the probability of a proton fusing is 10-19 per proton per second (that’s hundreds of billions of years before fusing)
As a result, the sun produces around 250W per cubic meter
On earth, we need a much more efficient reaction!
Notes: The first problem with magnetic confinement is fundamental - no matter how strong or well formed the magnetic field containing the plasma is, it will always leak, as positive nuclei or ions spiralling around the magnetic field lines collide and scatter, eventually drifting out of the containment field. The only known solution is to make the reactor larger so the scattering ions take longer to travel to the plasma boundary, and thus more fusion can happen during that time.
A more practical problem is how do we extract the energy? Most of the energy in deuterium-tritium fusion reactions is released in fast, high-energy neutrons, which (because they are neutral, and have no electric charge) are not confined by the magnetic field, don't heat up the plasma, and have to be stopped by a thick shield, which then heats up, and can vaporize water to steam in order to power turbines and electrical generators. The problem is the constant bombardment by neutrons makes the shield material degrade with time, and become very radioactive, posing a problem for removal and disposal.

## Slide 4: Why is fusion hard to achieve?
Requirements of a nuclear fusion device:
Plasma ~100M°K to overcome Coulomb forces
Keeping burning hot plasma levitating in the vacuum without touching the walls
Materials must withstand neutron bombardment, intense heat, and mechanical stress
Produces energy indefinitely with energy produced/energy injected >> 20
We use magnetic fields to contain the plasma
Using a tokamak or a stellarator
Magnets generating fields of 5 to 12 Tesla
  Superconducting
  cooled at 4K
Fusion power output scales strongly with magnetic field strength
Plasma is intrinsically unstable and needs to be tightly controlled by the magnetic fields
100M°K
4°K
The ITER Tokamak
Notes: The first problem with magnetic confinement is fundamental - no matter how strong or well formed the magnetic field containing the plasma is, it will always leak, as positive nuclei or ions spiralling around the magnetic field lines collide and scatter, eventually drifting out of the containment field. The only known solution is to make the reactor larger so the scattering ions take longer to travel to the plasma boundary, and thus more fusion can happen during that time.
A more practical problem is how do we extract the energy? Most of the energy in deuterium-tritium fusion reactions is released in fast, high-energy neutrons, which (because they are neutral, and have no electric charge) are not confined by the magnetic field, don't heat up the plasma, and have to be stopped by a thick shield, which then heats up, and can vaporize water to steam in order to power turbines and electrical generators. The problem is the constant bombardment by neutrons makes the shield material degrade with time, and become very radioactive, posing a problem for removal and disposal.

## Slide 5: A sun in a bottle?
Long Timelines & Costly Prototypes
Each physical test or reactor build takes years and billions of dollars.
Uncertainties in plasma behavior make experimental design and scaling difficult.
Complex, Multiphysics Simulations
Fusion involves magnetohydrodynamics, nuclear reactions, turbulence, plasma-wall interactions, etc…
No single model can capture all physics at all scales
requires multi-scale, multi-physics coupling
Scientific AI to the rescue!
x
x
Notes: The first problem with magnetic confinement is fundamental - no matter how strong or well formed the magnetic field containing the plasma is, it will always leak, as positive nuclei or ions spiralling around the magnetic field lines collide and scatter, eventually drifting out of the containment field. The only known solution is to make the reactor larger so the scattering ions take longer to travel to the plasma boundary, and thus more fusion can happen during that time.
A more practical problem is how do we extract the energy? Most of the energy in deuterium-tritium fusion reactions is released in fast, high-energy neutrons, which (because they are neutral, and have no electric charge) are not confined by the magnetic field, don't heat up the plasma, and have to be stopped by a thick shield, which then heats up, and can vaporize water to steam in order to power turbines and electrical generators. The problem is the constant bombardment by neutrons makes the shield material degrade with time, and become very radioactive, posing a problem for removal and disposal.

## Slide 6: How can Scientific AI help?
Uncovering Hidden Patterns
AI analyzes high-dimensional data for correlations humans or standard equations might miss, refining the next HPC simulations.
Surrogate Modeling
AI learns from massive datasets to create fast approximations of plasma behavior, cutting compute times.
Faster Iteration
Combining AI predictions with HPC accuracy accelerates design improvements.
Real-Time Control
Traditional HPC codes can’t adapt quickly; AI-driven models detect potential disruptions and propose magnetic/fueling adjustments in real time.
“Magnetic control of tokamak plasmas through deep reinforcement learning”, Federico Felici at a., Nature, 2022
ASCOT5 particle tracking simulation code

## Slide 7
Training
Inference

## Slide 8: SCITAS HPC&AI Infrastructure
Tightly coupled, Centralized High Performance Storage
GPFS high throughput, low latency FS though Infiniband
Tiered Production Pipeline:
CPU cluster: pre/post-processing, large-scale simulations, orchestration
RTX 6000 Pro + L40S: interactive work, visualization, data prep, medium-scale AI, inference, Digital Twins
H100: large-scale simulations, hybrid HPC/AI, fine tuning and acceleration
B200: frontier-scale AI training and foundation models
Seamless Cloud Access
Access to “exotic” and remote hardware
Usage peak absorption

## Slide 9: EUROfusion Digital Twins
EUROfusion Digital Twin Proof of Concept coupling:
a SOLPS-ITER code surrogate model,
the ANSYS CAD/Finite element analysis software,
the DEFUSE fusion database analysis framework,
a UNREAL 5-based fusion plasma renderer,
Nvidia Omniverse.
The objectives are:
Develop a platform coupling multi-physics, engineering and visualization tools
Assess the numerical uncertainty, reliability, robustness and performance optimization of the divertor of the TCV tokamak

## Slide 10: Thank you! Real-time Digital Twin (eM+/SPC)